## Slide 1: MQTT Workshop
By : Herm lecluse & tom verstraten
Notes: tom

## Slide 2: MQTT
Message Queue Telemetry Transport
IoT
Ideal for m2m
Protocol
TCP based
Notes: tom

## Slide 3: Some specifics
Topic
Publish/Subscribe based
Lightweight
Broker/client
Notes: Herm tekenen

## Slide 4: Publish/ Subscribe
Client subscribes to a topic on the broker
Can be any given name
Paths are recommended
  Using paths, wildcards can be used (#)
Client will receive any message sent in one of the subscribed topics.
Publish will send a message to all subscribers
Notes: herm

## Slide 5: Why MQTT?
Simple to implement
Central broker
QoS, More on that in the next slide
Subscription Pattern for easy filtering
Extremely Lightweight
Ideal for low bandwidth/high latency networks
Continuous Session Awareness
Can be encrypted using SSL/TLS
Notes: tom

## Slide 6: Qos
QoS 0 – at most once PUBLISH
  Fire and forget
QoS 1 – at least once PUBLISH  PUBACK
  Message delivery is confirmed by receiver.
  After given time broker will retry sending
QoS 2 PUBLISH  PUBREC PUBREL  PUBCOMP
  Safest and slowest
  Message will only be delivered once
Notes: Tom Tekenen

## Slide 7: Other features
Persistent sessions  subscribed topics and queued messages will be stored on reconnect
Last Will
  Notify other devices
Keep Alive
Notes: herm

## Slide 8: frameworks
PAHO eclipse – client
  Open Source client implementation
Mosquitto – broker
  Open source broker implementation
  Also provides a Raspberry implementation!
  Low power devices
Pre-implemented MQTT protocol.
Notes: herm

## Slide 9: Connecting a client
Create a new PAHOClient and connect this to a broker address.
Call the connect method
Notes: tom

## Slide 10: Subscribing to a Topic / Publishing
Create a new ChatCallback
Subscribe to a topic and include the ChatCallback
Add the object as listener to receive message events.
Simply call the Publish method with a Topic and a Message to send a message
Notes: tom

## Slide 11: Exercise
Open the exercise using GitHub
Use classmates and experiment using the client.
MQTTLens is a really cool Chrome plug-in to check if your implementation functions as requested.
You can also set up your own mosquito broker.
Follow the guide for your OS at : https://mosquitto.org/download/

## Slide 12: Thank you!
Thank you for participating in this workshop.